## Slide 1: Zerto DRaaS & Intra Cloud Architecture
ZVM
ZVM
Customer A
vCenter
VM
VRA
VM
VRA
ZVM
Customer B
SCVMM
VM
VRA
VM
VRA
ZVM
DRaaS Cloud
vCenter
VRA
VRA
BC/DR Cloud
vCenter
VRA
VRA
ZCM
ZCC
ZCC
vCD
For each customer & cloud vCenter/SCVMM Zerto Virtual Manager (ZVM) & VRAs Install in minutes
Manager of managers
Zerto Cloud Manager
vCD, multi-tenancy, resource mgmt
Deploy dedicated port group Zerto Cloud Replication Network
Standard or distributed switch
For DRaaS multi-tenancy, 1 per customer
Zerto Cloud Connector (ZCC) 2 IPs, 1 customer facing 1 replication network
VPN, MPLS

## Slide 2: How to grant O2M/LTR features to the Customer
Required:
  CSP must have a CloudO2M license
  Customer ZVM must have a DRaaS-E license
How does the customer get a DRaaS-E license?
  CSP must register the ZORG on the Tenants Portal with a Product Type of Mulitcloud
  Once this is saved, it will send a Saleforce task to the Cloud Architect to create the DRaaS-E license.
  The Cloud Architect creates and sends the license to the CSP, who then implements that on the customer ZVM (site settings)

## Slide 3: CSP Licensing Scenarios

## Slide 4: DRaaS use case 1 Local copy for DRaaS customer using O2M

## Slide 5: Scenario 1.1: Local copy
DR site with CloudO2M license
ZVM
Site-1
On-Premise Hypervisor based
DR-Site managed by CSP
ZCM
DRaaS-E sublicense
ZCC
ZORG required
UNDER NDA – ZERTO Private and confidential
Notes: Most popular use case: loopback copy

## Slide 6: Scenario 1.2: Copy to another Enterprise site
DR site with CloudO2M license
ZVM
Site-1
On-Premise Hypervisor based
DR-Site managed by CSP
ZCM
ZCC
Site-2
DRaaS-E sublicense
DRaaS-E sublicense
ZORG required
UNDER NDA – ZERTO Private and confidential
Notes: Local copy to another enterprise site

## Slide 7: DRaaS use case 1.3 Multiple copies for DRaaS customer using O2M

## Slide 8: Scenario 1.3: Multiple copies to two CSP sites (multi-geo)
DR site with CloudO2M license
ZVM
DR-Site managed by CSP
ZCM
ZCC
DR site with CloudO2M license
ZVM
ZCC
DRaaS-E sublicense
On-Premise Hypervisor based
Site-1
Site-2
ZORG required
UNDER NDA – ZERTO Private and confidential
Notes: Optional slide, use to verify expectations of the call if needed.

## Slide 9: DRaaS use case 1.4 Inter-cloud (ICDR) protection to multiple sites

## Slide 10: Scenario 1.4: Multi-geo ICDR -- Hosting site to other CSP sites
DR site with CloudO2M license
ZVM
All managed by CSP
ZCM
DR site with CloudO2M license
ZVM
Site-2
Site-3
PROD site with CloudO2M license
ZVM
Site-1
ZORG required
UNDER NDA – ZERTO Private and confidential
Notes: Optional slide, use to verify expectations of the call if needed.

## Slide 11: ECE to CSP Use Case 2 Existing ECE customer with active Maintenance and Support

## Slide 12: Scenario 2.1: Add replication to CSP site
DR site with CloudO2M license
ZVM
Site-1
On-Premise Hypervisor based
DR-Site managed by CSP
ZCM
ZCC
Site-2
ZVR ECE license
ZVR ECE license
ZORG required
UNDER NDA – ZERTO Private and confidential
Notes: Local copy to another enterprise site

## Slide 13: Scenario 2.2: Retire on-premises site
DR site with CloudO2M license
ZVM
Site-1
On-Premise Hypervisor based
DR-Site managed by CSP
ZCM
ZCC
Site-2
ZVR ECE license
ZVR ECE license
ZORG required
UNDER NDA – ZERTO Private and confidential
Notes: Local copy to another enterprise site

## Slide 14: Do’s and Don’ts for CSPs
Use the ZCM to maintain ZORGs and deploy ZCCs
  ZORGs are required for One-to-Many licensing
  ZORGs are required for BYOL program
  ZORGS will be required to grant access to Analytics portal
Enable CallHome
  Required for Billing
  Required to receive compatibility updates
Use the LogArchiver
  By default Logs only exist for 4 days and have a limit of 150 files

## Slide 15: Deep Dive ZCC

## Slide 16
Customer A
Customer B
ZCC A
ZCC B
4007 / 4008
4007 / 4008
4007 / 4008
4007 / 4008
4007 / 4008
4007 / 4008
4007 / 4008
4007 / 4008
4007 / 4008
9082 / 9083
9084 / 9085
9082 / 9083
9084 / 9085
9086 / 9087
9082 / 9083
9084 / 9085
9086 / 9087
9088 / 9089
9082 / 9083
9084 / 9085
9086 / 9087
9088 / 9089
CSP
ZCC Traffic Flow for ICDR and DRaaS
All traffic is bi-directional

## Slide 17
The purpose of the ZCC is to provide CSPs with support for overlapping IP ranges in end-customer environments

## Slide 18: Core Implementation
The ZCC acts as a network proxy between the CSP entities (ZVM + VRAs) and the end-customer entities
  Two NICs: one in the CSP’s network (eth0) and one in the customer’s (eth1)
  Connecting to the customer’s network implies a VPN
The ZCC serves a variable number of entities, and therefore handles multiple ports
One ZCC per end-customer-ZVM

## Slide 19: Core Implementation – Conceptual View – Zoom In
A ZCC port is “mapped” to an address + port of an entity (ZVM / VRA)
ZCC
ZVM
VRA
VRA
9082
9084
9081
9081
4007
4007
VRA
CSP
Customer
The customer VRA only connects to the “customer side” address of the ZCC

## Slide 20: Core Implementation – Packet Flow
The ZCC relies on Network Address Translation / Port Address Translation (NAT/PAT) for achieving its goal
  Implemented by iptables (Linux user-space command-line tool for configuring the Linux kernel firewall)
  Two NAT rules are applied as a packet is processed: Destination NAT (DNAT) and Source NAT (SNAT)

## Slide 21: Core Implementation – Extra Credit…
Q: Packet leaves the ZCC and reaches CSP VRA. How is the reply sent back? Where is the rule that maps port 10112 back to the customer VRA?
A: The Linux firewall is stateful: it allocates a port when a TCP connection is established, and remembers it for the lifetime of the connection.
VRA
4007
VRA
From: 172.16.2.3:10112
To: 172.16.1.5:4007
172.16.1.5
10.0.0.3
9082
ZCC
172.16.2.3
10.0.0.2

## Slide 22: Core Implementation
The ZCC lets CSPs support end-customers with overlapping IP subnets
  One ZCC per end-customer-ZVM
  ZCC has two NICs: one in the CSP’s network, the other in the end-customer’s
Packets forwarded through DNAT and SNAT rules
  DNAT rule - eth1:9082 -> 172.16.1.5:4007
  SNAT rule - eth0 -> 172.16.1.3:10000-60000
One port on the CSP NIC for each entity-port on the customer side, and vice-versa

## Slide 23: ZCC Flows – Installation
ZCC installation is initiated from the ZCM in DRaaS scenarios
  Performed in the context of a specific ZORG
  User must select a (cloud) site, i.e. a ZVM, in which the ZCC will be installed

## Slide 24: ZCC Flows – Installation
Installation flow:
  Deploy ZCC OVF with bootstrap disk:
    Configure network parameters
    Block SSH from customer side
    Configure SNAT rule in both directions
    Starting Balvenie: inject ZVM’s public key to allow SSH without credentials
    (Not a complete list)
  Configure vShield for vCD
  Power on
  Configure over SSH initial DNAT rule: eth1:9081 -> CloudZVM:9081
  ZCC is associated with a ZORG even before pairing

## Slide 25: ZCC Flows – Installation
On the Customer (Organization Network) side, the CSP can configure a default gateway

## Slide 26: ZCC Flows – Installation
On the CSP (Cloud Network) side, the CSP can configure a static route group

## Slide 27: ZCC Flows – Installation – Routing
Static Route Groups are sets of routing rules that can be applied to ZCCs
Static Routes are configured from Site Settings

## Slide 28: ZCC Flows – Installation – Routing
In the installation workflow, a default gateway applies to the end-customer network while static route groups apply to the CSP’s network
Q: In the ZCC network configuration, what ties the route groups to eth0 (the NIC on the CSP-side)?
A: Nothing! The default gateway can just as well belong to the CSP’s network, and the static route groups can belong to the end-customer’s network
  … but this is against convention.

## Slide 29: ZCC Flows – Installation - Failures
In case of a failure after the deployment of the OVF, the ZCC VM is not cleaned up and the ZCC in an “Orphaned” status
  The most common cause for this is failure of the ZVM to SSH to the ZCC in order to configure the rules
  Leaving the ZCC VM alive allows the CSP to perform network troubleshooting to track down the problem
An Orphaned ZCC can only be uninstalled

## Slide 30: ZCC Flows – Installation – vCD
With vCD, customers set up a VPN to connect their on-premise network to their org vDC network. The ZCC will then connect to the org vDC network:
Customer A
VRA
VRA
ZVM
10.0.0.1
Cloud
VRA
VRA
ZVM
172.16.1.5
Internet
ZCC
172.16.2.3
10.0.0.2
VPN GW
VPN GW
VM
VM
…
VM
Customer VMs

## Slide 31: ZCC Flows – Installation – vCD
During ZCC deployment we still list only VC portgroups
Due to the vCD naming scheme, they can easily(?) be mapped to the corresponding org vDC network

## Slide 32: ZCC Flows – Installation – vCD

## Slide 33: ZCC Flows – Installation – vCD
Q: Is this really how CSPs running vCD with many customers select the correct network during ZCC deployment?
A: Yes!

## Slide 34: ZCC Flows – Installation – vCD (extra credit)
Org vDC networks in vCD are ultimately portgroups in VC, but they are isolated by VCNS / NSX:
Customer A
VRA
VRA
ZVM
10.0.0.1
Cloud
VRA
VRA
ZVM
172.16.1.5
Internet
ZCC
172.16.2.3
10.0.0.2
VPN GW
VPN GW
VM
VM
…
VM
Customer VMs
Org vDC network
Isolated portgroup
Unisolated portgroup

## Slide 35: ZCC Flows – Installation – vCD (extra credit)
Connecting the ZCC to an isolated portgroup will still not(!) let it see the traffic going through the portgroup
  We need to attach the ZCC to the “virtual network ID” (virtual wire in VXLAN)
This requires knowing the virtual network ID and adding fields to the ZCC’s VM configuration in the MOB
How can we learn the virtual network ID?

## Slide 36: ZCC Flows – Installation – vCD (extra credit)
We steal it from other VMs connected to the same network!
  … so this won’t work if there are no VMs connected to the org vDC network
The MOB’s values can be found under the VM’s extraConfig and are called ethernet{0}.filter{1}.name / param0 / param1

## Slide 37: ZCC Flows – Uninstallation
ZCC uninstall is initiated from the ZCM
Uninstall removes the ZCC VM and clears it from the ZVM DB
Q: What happens if a site is paired through the uninstalled ZCC?
A: It loses connectivity, even if the ZCC is then reinstalled. Later we’ll see why.

## Slide 38: ZCC Flows – Repair/Redeploy
If a ZCC VM is deleted from vCenter, the ZCC enters a Ghost state
A Repair operation can be initiated from the ZCM if the ZCC is ghosted
The user can change the host/datastore/network selections of the ZCC, but cannot change the ZORG association
After the new ZCC is deployed, all existing rules will be re-applied
Note: before 5.0u1, static route groups were not applied during Repair (bug 13646)

## Slide 39: System Flows – Pairing
ZCC rules are required to pair a customer ZVM with a CSP ZVM, but…
… we can’t set up the rules without knowing the customer’s ZVM IP
… we can’t know the customer’s ZVM IP before it reaches the cloud ZVM!
Solution: A ZCC is born with one DNAT rule: eth1:9081->cloud_zvm:9081
  Which connectivity does this enable?

## Slide 40: System Flows – Pairing – cont’d
When a ZVM receives a pairing request, it checks whether this request comes from a ZCC IP
If so, it retrieves the peer ZVM’s IP from the ZCC and sets up the reverse DNAT rule (eth0:9081 -> cust_zvm:9081) before reaching out to the customer ZVM
  It also associated the peer site with the ZCC’s ZORG
See:CloudConnectorManager.SetCustomerZvmIfHostIsCloudConnector, called by SiteOperations.ConnectAndValidate

## Slide 41: System Flows – Pairing – cont’d
How does the cloud ZVM obtain the peer ZVM’s IP?
It connects to the ZCC and runs a netstat-nat command to find all active connections that are currently being routed through the ZCC
  Which connection would you expect to find there?
  Note: starting 5.0, netstat-nat is a script written by Zerto; not part of the OS
It then takes the first connection in the list and retrieves its source IP
… what could possibly go wrong?

## Slide 42: System Flows – Adding a VRA
When a new cloud VRA is installed, a corresponding entry is added to all ZCCs belonging to the ZVM
When a new customer VRA is installed, a corresponding entry is added to the ZCC associated with the owning peer ZVM
See HostTracker.SetIPOnPeersOperation, AddPeerVraInfoTask.AddPeerVraInfoTaskFunc, PeerVraInfoSynchronizer.Synchronize, and RemoteSynchronizer.GetLocalVraInfo.

## Slide 43: System Flows – Adding a VRA
To decide on a port to use, the system takes the highest used port number and adds 1 (ports are not recycled!) – see PersistentNatTable.AddPortMapping.

## Slide 44: Implementation Details – Connectivity
The cloud ZVM uses SSH to connect to the ZCC and configure it
Before Balvenie, hard-coded credentials were used (root/zertodata)
  Starting Balvenie, public-key-based authentication is used by default
Excluding netstat-nat, all scripts and commands sent to the ZCC are configured by the ZVM (i.e. no scripts on the ZCC). See CommandLineScriptProvider and its inheritors.
  Anyone remember what netstat-nat does?

## Slide 45: Implementation Details – State
The ZCC is stateful: any rule changes are persistently stored, in the ZCC, using iptables-save (serialize to a file)
When the ZCC boots, it loads the rules from the serialized file using iptables-restore
There is no rule synchronization mechanism between the ZVM and ZCC
  If you want to force a resync, delete the ZCC VM from VC (don’t uninstall the ZCC!) and redeploy

## Slide 46: Implementation Details – Database Tables
CloudConnectorStorageObject – list of ZCCs and their settings
CloudConnectorRouteStorageObject – list of routing rules
CloudConnectorStaticRouteStorageObject – stores static route groups

## Slide 47: Implementation Details – Uninstalling a ZCC
Q: If a ZCC is uninstalled and reinstalled (with the same parameters), why isn’t connectivity restored?
A: Because the new ZCC is born with a eth1:9081->cloud_zvm:9081 rule, but no rule going back from cloud to customer.
  Manually adding the rule to the ZCC (and ZVM DB) should restore connectivity because the VRA IPs will be automatically sync’ed by the ZVMs

## Slide 48: Implementation Details
Relevant classes
  Installation: CloudConnectorInstaller, InstallCloudConnectorTask, CloudConnectorBootstrapScriptProvider
  Ongoing work: ActiveCloudConnector, PersistentNatTable, CloudConnectorSshConnectionFactory

## Slide 49: Troubleshooting
During log collection, the ZVM runs a bunch of troubleshooting commands on all ZCCs, resulting in a cloudconnectors.txt file containing:
  ifconfig output (NIC configuration)
  Dump of iptables rules (same verbose format we saw earlier)
  Output of netstat / netstat-nat
  Output of route (routing table)
This is incredibly useful – use it!
Note: duplicate rules are not a problem (but they are a bug)

## Slide 50: Troubleshooting
Q: If pairing through a ZCC fails, which connectivity tests should you run?
A: Several:
  From the ZCC, ping cloud ZVM
  From the ZCC, ping customer ZVM
  From the customer ZVM, telnet to ZCC’s customer leg on port 9081
But do not:
  From the cloud ZVM, telnet to ZCC’s cloud leg on port 9081
  From another customer machine, telnet to ZCC’s customer leg on port 9081
  Why?
Notes: No point telnet’ing to the cloud leg on port 9081, because the only rule that exists is eth1:9081 -> cloud_zvm:9081. The ZCC isn’t listening on port 9081 of the cloud leg, and it’s not forwarding the traffic, either.
If you telnet to customer_leg:9081 from another machine, you’ll reach the cloud ZVM and *create a connection on the ZCC*. When you then pair again, the “customer ZVM IP detection mechanism” can get confused! If this happens, easiest thing is to delete the ZCC and redeploy. If you made this mistake, you will see in the logs of the cloud ZVM that it wrongly detects the customer ZVM IP address.